## Slide 1
Chandra X-ray Observatory Operations

## Slide 2: Overview
1. Mission and Observatory Description
2. Chandra Operations
3. Chandra X-ray Center Architecture
4. Mission Metrics
5. Operational Process Example - Reacting to Radiation Belts

## Slide 3: NASA’s Great Observatories
CHANDRA

## Slide 4: Chandra Mission Summary
Launch July 23, 1999
  STS-93/ Inertial Upper Stage / Integral Propulsion System
  10,000 km x 140,000 km, 28.4o Inclined Orbit
Design Lifetime > 5 Years
10-m Focal Length Wolter -1 Mirror: 4 nested Mirror Pairs
Energy Range: 0.1-10 KeV
2 Imaging Focal Plane Science Instruments
  ACIS (Advanced CCD Imaging Spectrometer)
  HRC (High Resolution Camera)
2 Objective Transmission Gratings for Dispersive Spectroscopy
  LETG (Low-Energy Transmission Grating)
  HETG (High-Energy Transmission Grating)

## Slide 5: 1. Mission and Observatory Description

## Slide 6: Chandra Science Instruments
Advanced CCD Imaging Spectrometer (ACIS)
  CCD array with 16’x16’ field of view (ACIS-I)
  high energy grating readout array (ACIS-S)
High Resolution Camera (HRC)
  microchannel plate imager with 31’x31’ field of view (HRC-I)
  low energy grating readout array (HRC-S)
High Energy Transmission Grating Spectrometer (HETG)
  transmission grating pairs for medium and high energy
Low Energy Transmission Grating Spectrometer (LETG)
  transmission grating for low energy
ACIS-I
ACIS-S
HRC-I
HRC-S

## Slide 7: Chandra Launch
Launched on Space Shuttle Columbia 7/23/99 on the third attempt
Shuttle placed Chandra and IUS in 150 mile orbit
Chandra was the longest and heaviest payload launched on the Shuttle
Payload bay doors open 1.5 hours after launch
Chandra/IUS deployed 7.5 hours after launch

## Slide 8: Chandra Deployment and Orbit
Inertial Upper Stage (IUS) boosted Chandra from shuttle orbit to transfer orbit. Two stage rocket with two 2 minute burns.
Chandra separated from the IUS 9.5 hr into mission with orbit of 300km x 74,000km
Chandra’s Integral Propulsion System fired 5 times over 15 days to reach final orbit: 10,000 km x 140,000 km. Orbit of 64 hrs and going 1/3 of way to moon

## Slide 9: 2. Chandra Operations
Mission science plan converted to command loads and uplinked to Chandra
X-ray events collected and stored on Solid-State Recorders (SSR)
Ground contact established every ~8 hours through Deep Space Network
  SSR data downlinked
  new command load uplinked (up to 72 hours of stored commands)
Data transferred to OCC through JPL for science processing
CXO
CXC
OCC
ssssssssssssssssssssss

## Slide 10
S/C Support &
Eng Analysis
Attitude Det. &
Sensor Cal
Mission Planning
& Scheduling
Command
Management
Data Capture
Telemetry
Processing
Command
Processing
Communication
Ops
Simulator
Operations
Database
Off-Line System
On-Line System
Flight S/W Maint Fac
IPIs, Guest Observers
CXC
Observation Request
Mission Schedules
Telemetry
Proposed Observation
Science Data
S/W Changes
Telemetry
Commands
DSN Scheduling
State Vector
Telemetry
Commands
Deep Space Network
Deep Space Network
Telemetry
Commands
(Via Shuttle)
Telemetry
Commands
OCC
Chandra

## Slide 11: 3. Chandra X-ray Center Architecture

## Slide 12: CXC Pipeline Processing
Data processed through levels
  Level 0 - De-commutates telemetry & processes ancillary data
  Level 1 - Event processing
  Level 2 - Source detection and derived source props
  Level 3 - Catalogs spanning multiple observations
AP System comprised of series of pipelines controlled through registry and Observation Status Tracker
Pipeline defined by ASCII profile containing a list of tools and parameters specified at run-time
Pipeline profile executed by Pipeline Controller
Profiles and Controller are configurable and support
  conditional execution of tools
  branching and converging of threads

## Slide 14
Cycle 1 Observing Efficiency
(Nov. 1 1999 - August 15, 2000)
4. Mission Metrics

## Slide 16: Chandra Archive
Chandra telemetry rate 32 KB/s results in ~120 Gby/yr telemetry
Expansion from telemetry to processed products ~10:1
Archive ~650 Gby after 14 months with ~2:1 compression
Growth rate of ~500 Gb/yr or ~1 Tby/yr uncompressed
Average of 25 Gby/month retrieved; range of 6-60 Gby

## Slide 17: 5. Operational Processes: Example
Degradation in the ACIS energy resolution of front side chips detected as increase in Charge Transfer Inefficiency in September 1999. Backside chips (S1 and S3) unaffected.
Degradation due to low energy protons (~100 keV) focussed by mirror during radiation belt passage
Halted by moving ACIS out of focal plane during radiation belt passage
Effect can be offset by reduced focal plane temperature and via ACIS flight software changes, e.g., “squeegee mode” under development
Multiple operational impacts required systems approach to respond efficiently

## Slide 18: Implications and Response
Operational implications
  Modified mission scheduling to ensure ACIS safed for belt passages & added CTI measurements: efficiency impact
  Spacecraft software changes to protect Instruments in the event of spacecraft safing action
  Modified ACIS, ground operations and science processing software
  Modified observing program for optimal chip usage
  Developed new calibration program
  Real-time alerts from
  solar monitoring data & models
Single anomaly resulted in system-wide changes and response
Include system case in ops design